## Slide 1: STM8 8-bit MCU Family

## Slide 2
More than one million units delivered worldwide every day! We plan for longevity with a sustainable growth
STM8 series
STM8 MCU LONGEVITY COMMITMENT
STMicroelectronics provides a minimum longevity of 10 years for its STM8 microcontrollers!
STM8AF series of multi‑purpose 8‑bit microcontrollers for automotive applications
STM8AL series of ultra‑low‑power 8‑bit microcontrollers for automotive applications
STM8L series of ultra‑low‑power 8‑bit microcontrollers
STM8S series of mainstream 8‑bit microcontrollers
STM8

## Slide 3
STM8 CORE
ST’s 8‑bit microcontroller platform is implemented around a high‑performance 8‑bit core and a state‑of‑the‑art set of peripherals. This platform is manufactured using an ST‑proprietary 130 nm embedded non‑volatile memory technology. It is able to reach 1.6 cycles per instruction and up to 24 MHz clock frequency, allowing customers to run their applications at low speed with high performance.
The lexibility of the architecture minimizes switching noise, resulting in improved system robustness and lower power consumption.
An innovative clock implementation provides strong beneits such as fast wake‑ups in only 4 μs.
It enables immediate clock switching on the ly to allow clock accelerations for PWM or calculation routines.
The 32‑bit robust NVM memory addressed through a 3‑stage pipeline interface, the 16‑bit index registers and stack pointers and the advanced instruction set with hardware
multiplication/division are key elements that signiicantly improve the eficiency of this 8‑bit device family.
STM8 series
STM8 core
Fetch
Decode
Execute
3-stage
pipeline
Complete instructions
32-bit memory
Data memory
B4 | B3 | B2 | B1
The STM8 allows fast and safe development through enhanced stack pointer operations, advanced addressing modes and new instructions.

## Slide 4
STM8 series
STM8S
Mainstream
STM8 S
Data EEPROM,
3 and 5 V families, precise RC
STM8A
Automotive
STM8 A
Data EEPROM,
3 and 5 V families, precise RC, LIN, CAN, grade 0
STM8L
Ultra‑low‑power
STM8 L
Data EEPROM,
1.65 and 3 V families, strong analog, LCD drivers, low-leakage technology
Best market value
Long‑term guarantee
Ideal combination of low‑power performance and features
Robust and reliable Up to 125 ° C www.st.com/stm8s
AEC-Q100
Up to 150 °C www.st.com/stm8af www.st.com/stm8al
High-end analog IPs Active Halt < 1 μA www.st.com/stm8l

## Slide 5
STM8 series
CAN
2- to 64-Kbyte,
20- to 80-pin
LCD AES
LIN
Mainstream
Automotive
Ultra-low-power
Standard
Ultra‑low‑power
General purpose
Performance
Value
Speci c
4- to 128-Kbyte,
20- to 80-pin
STM8S903
STM8S003
STM8S005
STM8S007
STM8S103
STM8S105
STM8S207
STM8S208
4- to 128-Kbyte,
20- to 80-pin
STM8AL31
STM8AL3L
STM8AL3LE
STM8AL31E
STM8AF62
STM8AF52
STM8L051
STM8L052
STM8L101
STM8L151
STM8L152
STM8L162
PORTFOLIO OVERVIEW
A large product portfolio to meet all your needs

## Slide 6
STM8 series
STM8S DESCRIPTION
Upgrade to a higher or downgrade to a lower memory size, or use a different package across lines without changing the initial layout or software.
STM8 24 MHz CPU
4 to 128 Kbytes of embedded Flash memory, up to 6 Kbytes of SRAM
Supply voltage: 2.95 to 5.5 V
Up to four low‑power modes: down to 4 µA with complete context retention
State‑of‑the‑art digital and analog peripherals
Speciic interfaces such as IrDA and smartcard for support of consumer applications
‑40 to +85 °C, or up to 125 °C temperature range
Free class B self‑diagnostic library for IEC 60335/IEC 60730 compliant applications
Many software libraries and examples are available for download
STM8S APPLICATIONS
Appliances, power tools
HVAC
Power management
Lighting
Factory automation
Devices with rechargeable batteries
Motor control
e‑vehicles
Toys and games
Sensors
Power supplies
User interfaces

## Slide 7
STM8 series
CAN 2.0 B
2xU(S)ART LIN
Smartcard / IrDA
Connectivity
SPI
I²C
Boot ROM
Up to 2-Kbyte EEPROM
4- to 128-Kbyte Flash memory
Up to 6-Kbyte SRAM
Analog
10-bit ADC 16 channels
STM8 CPU
Up to 24 MHz
Nested vector interrupt controller (NVIC)
SWIM debug module
Control
System Power supply
2x16-bit timer 2/3 CAPCOM
Beeper 1/2/4 kHz
8-bit timer
16-bit timer, 4 CAPCOM + 3 comparator outputs
AWU
Clock detector
2.95 to 5.5 V
(1.8 V internal regulator) POR / BOR
Xtal oscillator
1-24 MHz
Internal RC oscillators 128 kHz and 16 MHz
Clock control
2x watchdogs (independent and window)
Up to 68 I/Os
STM8S BLOCK DIAGRAM

## Slide 8
STM8 series
STM8 core ‑ Up to 24 MHz
STM8S PRODUCT LINES
The STM8S series consists of four lines with differentiated features with full compatibility and upgradability to simplify design changes.
The STM8S003/005/007 Value line is the entry‑level series with a basic features set.
The STM8S103/105 Access line offers more features and a larger variety of packages.
The STM8S207/208 Performance line features a full set of peripherals and provides performance for medium to higher‑end applications.
The STM8S Application‑speciic line provides more analog features and dedicated irmware solutions.
10-bit ADC
USART, SPI, I²C
8- and 16-bit timers
16 MHz crystal oscillator and 128 kHz internal RC oscillators
SWIM debug module
Product line | FCPU (MHz) | Flash RAM memory (Kbytes) (Kbytes) |  | Data EEPROM (bytes) | CAN 2.0B | 2nd UART | Additional analog channels | LNB irmware
STM8S003/005/007 Value line | 16 | 8 to 64 | 1 to 6 | 128 |  |  |  | 
STM8S103/105 | 16 | 4 to 32 | 1 to 2 | 640 to 1024 |  |  |  | 
STM8S207/208 | 24 | 32 to 128 | 6 | 1024 to 2048 | • | • | • | 
STM8S Application‑speciic line | 16 | 8 | 1 | 640 |  |  | • | •

## Slide 9
STM8 series
STM8S903F3 STM8S903K3 STM8S103F3 STM8S103K3
STM8S003F3 STM8S00KF3
STM8S105K6 STM8S105S6 STM8S105C6
STM8S005K6 STM8S005C6
16 K STM8S105K4 STM8S105S4 STM8S105C4
STM8S208S6
STM8S208C6
STM8S208R6
STM8S007C8
STM8S207K6
STM8S207S6
STM8S207C6 STM8S207R6
Pin count
Flash size (bytes)
32 K
8 K
STM8S208M8
STM8S208C8
STM8S208R8
STM8S208S8
STM8S207M8
STM8S207C8
STM8S207R8
STM8S207S8
STM8S208MB
STM8S208CB
STM8S208RB
STM8S208SB
STM8S207MB
STM8S207CB
STM8S207SB
STM8S207RB
64 K
128 K
Access line
Application specific line
Value line
Performance line
Legend:
STM8S PORTFOLIO
STM8S207K8
4 K | STM8S103F2 |  |  |  |  | 
 | 20 pins | 32 pins | 44 pins | 48 pins | 64 pins | 80 pins
 | TSSOP/QFN/SO | LQFP/QFN/SDIP | LQFP | LQFP | LQFP | LQFP

## Slide 10
STM8 series
Run mode dynamic consumption down to 150 µA/MHz
State‑of‑the‑art digital and analog peripherals
‑40 to +85 °C, or up to 125 °C operating temperature range
Free touch‑sensing library
LCD driver
AES‑128 encryption
STM8L DESCRIPTION
Upgrade or downgrade to a different memory size, or package across lines without changing your initial design or software.
STM8 16 MHz CPU
2 to 64 Kbytes of embedded Flash memory, up to 4 Kbytes of SRAM and up to 2 Kbytes of EEPROM
Four lines: pin‑to‑pin, software and peripheral compatibility
Supply voltage: 1.65 to 3.6 V
Up to four ultra‑low‑power modes: down to 350 nA with SRAM and context retention

## Slide 11
STM8 series
Connectivity
1 to 3x USART
1 to 2x SPI
Touch sensing Charge-transfer driver
up to 16 channels
Analog
12-bit ADC
25 channels
1 to 2x 12-bit DAC
2x comparators
Temperature sensor
Boot ROM*
1- to 2-Kbyte EEPROM*
2- to 64-Kbyte
Flash memory
1.5- to 4-Kbyte SRAM
4-channel DMA
LCD driver
(4 x 28 or 8 x 40)
Display
Nested vector
interrupt controller (NVIC)
SWIM debug
module
STM8 CPU
Up to 16 MHz
RTC*/AWU
18/26/30/41/54/68 I/Os
System Power supply
1.8 V regulator POR/PDR/PVD/BOR
Xtal oscillator
32
kHz + 1~16 MHz
Internal RC oscillators
38 kHz + 16 MHz
Clock control
2x watchdogs
(independent and window)
Encryption AES (128 bits)
2 to 3x 16-bit timers
1x 8-bit timer
Control
1x 16-bit PWM
Synchronized AC timer
I²C
STM8L APPLICATIONS
Medical equipment
  Glucose meters and insulin pumps
  Blood pressure and colesterol monitors
  Patient monitoring
Metering (electricity/gas/water/ heat meters, and scales)
Alarm systems (central units, sensors, door locks, and ire alarms)
GP portable devices
  Mobile phones, and accessories
  Gaming and remote controls
GPS watches and sports equipment
Note: * STM8L15x/STM8L16x only
STM8L BLOCK DIAGRAM

## Slide 12
STM8 series
STM8L PRODUCT LINES
STM8 core – Up to 16 MHz
12-bit ADC
12-bit DAC
USART, SPI, I²C
RTC with 32 kHz oscillator
8- and 16-bit timers
Temperature sensor
Comparators
SWIM debug module
Product line | Flash memory (Kbytes) | RAM (Kbytes) | Data EEPROM (bytes) | Four DMA channels | LCD interface | AES 128‑bit crypto
STM8L051/052 Value line | 8 to 64 | 1 to 4 | 256 | • | • | 
STM8L101 | 2 to 8 | 1.5 |  |  |  | 
STM8L151/152 | 4 to 64 | 1 to 4 | 256 to 2048 | • | • | 
STM8L162 | 64 | 2 | 2048 | • | • | •

## Slide 13
STM8 series
STM8L PORTFOLIO

## Slide 14
STM8 series
Typical current
@ 25 °C
Low-power Run
@ 32 kHz
5.1 µA
Dynamic Run from RAM
90 µA/MHz
Dynamic Run from Flash
192 µA/MHz
Low-power Wait
@ 32 kHz
3.0 µA
Active Halt with RTC
1.2 µA
Halt
0.3 µA
Notes:
POR/PDR on
RAM content preserved
BOR option at 2.4 µA
Startup time from Active Halt 5 µs
STM8L ULTRA LOW POWER MODES

## Slide 15
STM8 series
The STM8L series is available in four different lines making the STM8L an optimal series to support many applications requiring special care on power savings.
STM8L101 line
  Lowest power mode: 0.30 µA
  Dynamic run mode: 150 µA/MHz
STM8L151/152 line
  Lowest power mode: 0.35 µA
  Dynamic run mode: 180 µA/MHz
STM8L162 line
  Lowest power mode: 0.35 µA
  Dynamic run mode: 180 µA/MHz
STM8L051/052 Value line
  Lowest power mode: 0.35 µA
  Dynamic run mode: 180 µA/MHz
STM8 L
STM8L ULTRA LOW POWER MODES – BY FAMILY

## Slide 16
STM8 series
STM8S‑DISCOVERY STM8SVLDISCOVERY
STM8A‑DISCOVERY
STM8 A
STM8L‑DISCOVERY
STM8 L
STM8 S
ORDERING INFORMATION
Order number Description | 
STM8S‑DISCOVERY | Discovery kit for STM8S series with STM8S105C6 MCU
STM8SVLDISCOVERY | Discovery kit for STM8S Value Line with STM8S105C6 MCU
STM8L‑DISCOVERY | Discovery kit for STM8L series with STM8L152C6 MCU
STM8A‑DISCOVERY | Discovery kit for STM8A Automotive series with STM8AF52C6 and STM8AL3L68 MCUs
STM8 TOOLS

## Slide 17
STM8 series
FREE TOOLS, SOFTWARE LIBRARIES AND EXAMPLES

## Slide 18
STM8 series
WEB TRAINING AND MATERIAL
Aside from all the available material from st.com/stm8
There is also some different Hands On trainings under our FAE’s repository here

## Slide 19: Thank You